Exposure control plan for cutting small amounts (< 3 square metres) of gypsum board containing asbestos

Cutting asbestos-containing gypsum board or drywall mud without proper controls can release asbestos fibres into the air. Breathing in asbestos fibres can cause asbestosis (a serious lung disease characterized by scarring and thickening of the lungs), mesothelioma, and other lung cancers. These diseases can result in death.

| This document will help contractors develop an exposure control plan (ECP) for work involving the cutting of small amounts (< 3 m2) of asbestos-containing gypsum board. An ECP is a requirement of the Occupational Health and Safety Regulation and sets out a detailed approach to protecting workers from harmful exposure to asbestos fibres. Contractors can use this document as a template and add specific details regarding their specific work practices. This document covers points you need to follow to protect workers from harmful exposure. It is important to follow all the points, at a minimum, or to use measures which are at least as effective. Tools and equipment for cutting gypsum board Knife Used to scribe gypsum board and snap or break it. If scribed and cut uniformly, gypsum board breaks cleanly. Generates the least amount of asbestos fibres. Hand-held gypsum board saws Useful for cut-outs, holes, and the removal of small amounts of gypsum board. Generates more dust than a knife. Kett saw A Kett saw is a small circular saw blade attached to a standard hand-held drill. When these saws are used, a dust collection system is required. Such a system includes an industrial vacuum cleaner equipped with a HEPA filtering system. The dust is collected and drawn into the vacuum, where it is filtered and the air is discharged. Vacuums Both dry and wet vacs may be used. These must be fitted with HEPA filtration to prevent asbestos fibres from entering the workplace air. Equipment tips Invest in good quality equipment and keep it well maintained. Well-designed and maintained equipment significantly reduces dust and lasts longer between replacement and maintenance. Respirator program Employers whose workers wear respirators are required to develop and implement a respirator program. The WorkSafeBC publication Breathe Safer provides guidance for developing this program. Additional information The following WorkSafeBC resources are available from WorkSafeBC.com. Safe Work Practices for Handling Asbestos book: http://www.worksafebc.com/publications/health_and_safety/by_topic/assets/pdf/asbestos.pdf Asbestos awareness bulletins: http://www2.worksafebc.com/Publications/Topic.asp?ReportID=34405 Asbestos in Demolition and Renovation slide show: http://www2.worksafebc.com/media/fss/asbestos/slideshow.htm Asbestos video: http://www2.worksafebc.com/Publications/Multimedia/Videos.asp?ReportID=35328 Notice of Project form for asbestos: http://www.worksafebc.com/insurance/managing_your_account/notice_of_project/default.asp Asbestos web site: http://www.hiddenkiller.ca/ For more information about health and safety, employers and workers can call the WorkSafeBC Prevention Information Line and ask to speak with an occupational hygiene officer. Call 604 276-3100 in the Lower Mainland or 1 888 621-7233 toll-free in B.C. Useful links UK Health & Safety Executive (HSE) asbestos health and safety web site: http://www.hse.gov.uk/asbestos/ CDC/NIOSH asbestos publications are available at: http://www.cdc.gov/niosh/topics/asbestos/ |  | Contractor company information Name Address Contact information (names and phone numbers) Worksite information Project name Address Health hazards from asbestos exposure Asbestos is a hazardous material. Its fibres are extremely fine and can remain suspended in the air for hours. Workers exposed to asbestos-contaminated air can inhale the fibres. If handled without precautions, such as appropriate respiratory protection, asbestos may cause serious chronic health problems or even death. Asbestosis is a chronic lung disease resulting from prolonged exposure to asbestos dust. The fibres gradually cause the lungs to become scarred and stiff, making breathing difficult. Asbestos fibres in the lungs may cause lung cancer. Smoking tobacco in combination with inhaling asbestos greatly increases the risk of developing lung cancer. Mesothelioma is a rare, rapidly progressing, malignant form of cancer affecting the lining of the chest or the abdominal cavity. There is a strong link between asbestos exposure and mesothelioma. Due to the relationship between asbestos exposure and cancer, exposure to asbestos fibres must be kept as low as reasonably achievable. Purpose and responsibilities We have a duty to protect our workers from exposure to asbestos fibres when asbestos-containing materials are disturbed. Studies show that the cutting or breaking of asbestos-containing gypsum board or drywall mud can release asbestos fibres into the air. Effective controls are available to protect workers from exposure to these fibres. We know that a combination of control measures will be required to achieve this objective. We commit to being diligent in our efforts to select the most effective control technologies available, and to ensure that the best practices, as described in this ECP, are followed at our worksites. The work procedures we establish for cutting asbestos-containing gypsum board will protect not only our workers but also all other workers on site. The employer is responsible for: Ensuring that the materials (i.e., tools, equipment, personal protective equipment) and other resources (i.e., worker training) required to fully implement and maintain this exposure control plan (ECP) are readily available where and when they are required. Conducting a periodic review (at least annually) of the effectiveness of the ECP. This includes a review of available asbestos control technologies to ensure these are selected and used when practical. Ensuring that all required tools, equipment, and personal protective equipment (PPE) are readily available and used as required by the ECP. Ensuring that supervisors and workers are educated and trained to an acceptable level of competency. Maintaining records of training, fit-test results, crew talks, and inspections (e.g., of equipment, PPE, and work methods/practices). Coordinating the work with other employers to ensure a safe work environment. Our asbestos program administrator [insert name here] is responsible for: Administering the overall program, including the maintenance of records Reviewing the program on an annual basis with the joint health and safety committee Supervisors are responsible for: Providing adequate instruction to workers on the hazards associated with the cutting of asbestos-containing gypsum board Selecting and implementing the appropriate control measures Ensuring that workers using respirators have been properly fit-tested and that the results are recorded Directing the work in a manner that ensures the risk to workers is minimized and adequately controlled Liaising with other employers to ensure a safe work environment Workers are responsible for: Using the assigned protective equipment in an effective and safe manner Following established work procedures as directed by the supervisor Reporting any unsafe conditions or acts to the supervisor Knowing how to report exposure incidents Risk identification and assessment Asbestos is a fibrous mineral that’s very tough and resistant to chemicals and heat. Up until 1990, it was regularly used in a large number of building products, including ceiling texture, drywall mud, flooring, and attic insulation. If these materials are disturbed (such as when they are drilled, sawed, sanded, or broken up during renovations or demolition), workers can breathe in asbestos fibres. If people breathe in enough asbestos fibres, their lungs can suffer damage, making breathing very difficult and potentially resulting in cancer and death. Gypsum board taping or finishing compounds (also known as drywall mud) can contain from less than 1% to 5% asbestos fibres. Rarely, the gypsum board itself may also contain small amounts of asbestos. When cutting asbestos-containing gypsum board, the use of proper dust controls, PPE, and safe work procedures can help reduce worker exposure to asbestos. Exposure limit The 8-hour occupational exposure limit (EL) for asbestos (all forms) is 0.1 fibres per millilitre (fibres/cc). As asbestos exposure is linked to lung cancer, the ALARA principle also applies, and workplace exposures must be reduced to levels as low as reasonably achievable. Control of asbestos fibres The Occupational Health and Safety Regulation requires employers to select asbestos controls based on the following hierarchy: Engineering controls (for example, local exhaust ventilation using a HEPA vacuum) Administrative controls (for example, cutting when other workers are not in the area) Personal protective equipment (for example, respirators and disposable coveralls) Respirators will be used in conjunction with other controls, such as local exhaust ventilation (LEV), to reduce worker exposure to asbestos fibres. A HEPA vacuum will be used for cleanup and decontamination. Acceptable control methods for cutting asbestos-containing gypsum board The work methods that appear in the table on page 4 are acceptable, provided that the respirator selection and other controls are adhered to. The control options on page 4 will be used to eliminate or reduce the risk to workers from the hazards of exposure to asbestos fibres. Work activity Dust suppression Other controls Personal protective equipment Small cuts of less than 1 square metre, using a knife or a hand-powered gypsum board saw Water misting Remove all unnecessary objects from the work area. Use plastic drop sheets. Use barriers (for example, a tape barrier) to restrict access to the work area and identify the hazard. Half-face respirator with P100 series (HEPA) filters Disposable coveralls (e.g., Tyvek type) Larger cuts (less than 3 square metres) or multiple cuts in one area, using a knife or a hand-powered gypsum board saw Water misting HEPA vacuum extraction Remove all unnecessary objects from the work area. Use plastic drop sheets. Use barriers (for example, a tape barrier) to restrict access to the work area and identify the hazard. Half-face respirator with P100 series (HEPA) filters Disposable coveralls (e.g., Tyvek type) with head covering Larger cuts (less than 3 square metres) or multiple cuts in one area, using a Kett saw HEPA vacuum extraction Remove all unnecessary objects from the work area. Use plastic drop sheets. Use barriers (for example, a tape barrier) to restrict access to the work area and identify the hazard. Half-face respirator with P100 series (HEPA) filters Disposable coveralls (e.g., Tyvek type) with head covering Respirators Each worker will be fit-tested if a respirator is required. If a worker is required to wear a respirator that requires an effective seal with the face for proper functioning, the worker must be clean-shaven where the respirator seals with the face. When the worker notices a resistance to breathing, the respirator filters must be replaced. Respirators will be used, cleaned, and stored in accordance with the respirator program. Other personal protective equipment and hygiene Workers will wear disposable coveralls (e.g., Tyvek) when working with asbestos-containing materials or entering a work area contaminated with asbestos. Other personal protective equipment, such as protective eyewear or hearing protection, will be worn as required. On active construction sites that require equipment such as hard hats or high visibility vests, this PPE will be worn in work or sampling areas. If equipment worn in a contaminated area cannot be adequately decontaminated, the equipment should be disposed of. Safe work planning Select one or more of the methods described in the table on page 4. Establish a barrier around the work zone to restrict access by unprotected workers. Place polyethylene sheeting below the work area to catch any debris released during the work activity. Inspect all dust-control equipment and tools to make sure they are in good working order. Use and maintain all tools and equipment as specified by the manufacturer. For example, test the effectiveness of HEPA filters using dioctyl phthalate (DOP) testing or similar means at least annually and any time a HEPA filter is replaced in a vacuum cleaner or ventilation system. When working on a multi-employer site, provide the general contractor with a copy of the asbestos exposure control plan and safe work procedures. Review the procedures and work schedule to determine if additional measures are required to reduce worker exposure to asbestos fibres. Ensure that workers inspect their respirators before start-up. If a Kett saw is used, visually monitor dust release from equipment during use. When tools and equipment are working properly, very little dust should be visible in the air. Stop work if excessive dust is observed. Cleanup and decontamination There are a number of different methods of decontamination. Selection of the correct method will depend on factors such as the work activities being conducted, the type of PPE worn, the nature of the containment, and the extent of the contamination. The following procedure can be considered a general guideline for decontamination after moderate-risk activities: All decontamination must take place within the restricted zone. Use a certified HEPA-filtered vacuum or wet methods (wash cloths, mops, etc.) to remove all visible asbestos materials in the work area. Wet-wipe all equipment and PPE. Wiping rags should only be used once. If using a bucket to wet the rags, wet the rags before wiping, and do not re-wet the rags. Damp-wipe the work area. Place waste material (including wipes) in a designated waste bag. Carefully roll up any polyethylene drop sheets and place in a designated waste bag. In a clean area, remove and discard disposable coveralls (and booties) in the designated waste bag. Use wash bucket and wet cloths to wipe any potentially contaminated exposed skin area (forehead, cheeks, etc.). Seal the waste bag, wet-wipe the outside of it, and then place it in a second bag. Label the outer bag to identify its contents, hazard(s), and the necessary precautions for handling the waste materials. All asbestos waste shall be disposed of in a duly authorized hazardous waste landfill. Remove and clean respirators. Use duct tape to cover HEPA cartridge inlets. Wash face, then hands. Worker training for asbestos exposure Training will be performed by the employer or the employer’s designate. Records of attendance, dates of training, and training material will be documented and retained. Additional training or reference material on asbestos exposure will be made available to employees upon request. Training topics: Asbestos recognition Health hazards of asbestos exposure (including signs and symptoms of asbestosis and mesothelioma) Operations and materials that can produce asbestos exposures Engineering controls and safe work practices used to protect workers The importance of proper equipment control and maintenance Proper use of respirators and the respirator program Personal hygiene procedures to reduce exposures The details of the exposure control plan for asbestos Health surveillance Workers who are regularly exposed to asbestos fibres will receive regular medical examinations from their family physicians. These examinations may include lung function testing and chest X-rays. Workers will report any symptoms of asbestos exposure to the employer and WorkSafeBC for tracking and investigation. Annual review This ECP will be reviewed at least annually and updated as necessary by the employer, in consultation with the workplace health and safety committee or the worker health and safety representative. |
| --- | --- | --- |